function [ vt tau fluxu fluxd ztropo z dz p rho mixh2o zb pb Tb rhob ...
    Tinit T Ts dE dEs dCE radu radd emitu sheat surfe TOAe TOAf TOAtr alr] =...
    HITRAN_0_10_1(dv, numz, mol, mix, ison, blp, BLH, FTH, contabs, linewon, Tsi, lapsekm, ...
    lapseikm, ptropo, minp, ocd, src, tstep, nt, ploton)
% Radiative transfer through atmosphere, up and down
% Uses the HITRANS database for absorption and emission lines with 
% Lorenzian broadening, not yet using Voigt profile; Pierrehumbert 2010 for
% continuum absorption.
% Generally creates a standard atmosphere of pressure, temperature to 
% calculate up and down spectral fluxes
% Can work from starting point to recalculate new temperature profile via
% "radiative convective" model using the defined lapse rate
% 
%
% v0.1 - Basic calculations to get out of the starting blocks
% v0.2 - Tidy up and allow a "slab" to be at any pressure and temperature
%       with line width determined by the pressure & temperature
% v0.3 - Allow multiple layers
% v0.4 - Orphan branch to evaluate wings of lines vs weak lines
% v0.5 - More GHGs, select which ones to pull data in
% v0.6 - Orphan branch not used here, adds CFC-11 & 12 which was difficult
%        because the minor GHGs are in a different database
% v0.7 - Dec 31st 2012, significant update to calc emission and absorption
%        through atmosphere (rather than just calc transmissivity) as a 
%        radiative-convective model
% v0.7.1- Added the energy absorbed/emitted by layer/wavenumber from
%        rte_0_5_3
% v0.8 - Set boundary layer top pressure so changes to no of layers doesn't
%        alter calcs (BLH can be different from FTH), fix stratosphere temp
%        in lieu of solar heating (via iso_strato parameter)
% v0.9 - Introduce continuum  absorption of water vapor
% v0.9.1- Adding some interim calcs like effective emission height, % of
%        emitted flux from each height that makes up TOA; likewise for DLR;
% v0.9.2- Clean up code comments for publishing, fix the calculation of 
%        layers just above the boundary layer (as noted by Frank), change 
%        surface pressure to 1013hPa, fixed convective adjustment to include 
%        the surface to first atmospheric layer, add different lapse rate  
%        for each layer
% v0.9.3- Allow stratosphere temp to move, but stay isothermal
% v0.9.4- Orphan version
% v0.9.5- Minor improvements and code efficiency suggested by Pekka
% v0.9.6- Change to input parameters to tidy up code - "mol" is a vector of
%         the HITRAN molecule numbers, to match vector "mix" which is the 
%         matching mixing ratio. This avoids editing code when different
%         GHGs are considered.
% v0.9.7- Added option to turn off line width formula, primarily to show
%         what happens when no narrowing of lines due to pressure (or
%         temperature changes)
% v0.10- Better tracking of heat movement when model run to equilibrium
%         Removed a few unnecessary variables passed back from function,
%         added comments for all variables passed back, note - Ts => Tsi in
%         this version
% v0.10.1- Added very basic parameterized solar heating by level, otherwise
%         other tradeoffs have to be made (e.g.,lose isothermal statrosphere)

% ====== Input conditions (passed to function) ====================
% dv =  resolution of wavenumber for calculations in cm^-1
% numz =  number of boundaries to consider (number of layers = numz-1)
% mol = vector of molecule # to be considered from HITRAN numbers: 1=H2O, 
%       2=CO2, 3=O3, 4=N2O, 5=CO, 6=CH4, must match mixing ration from
%       vector 'mix', e.g., mol=[1 2 4 6]; when mix=[0 360e-6 319e-9 1775e-9]
%       which means H2O (ignore because set by BLH/FTH), CO2 = 360ppm, N2O
%       = 319 ppbv, CH4 = 1775 ppbv
% mix = mixing ratio for each molecule as described for 'mol', but note
%       if first value is for H2O it is unused (BLH & FTH are used)
% ison = number of isotopes for each GHG, must match 'mol': 1 = only the
%       main is used), e.g., [1 1 1 1] means first isotopologue for the 
%       4 GHGs being; if mol=[1 2 3 4] & ison=[1 3 1 1] then CO2 will be
%       considered to the 3rd isotopologue but the others only to first
% blp = boundary layer thickness in Pa
% BLH =  relative humidity in the boundary layer
% FTH =  relative humidity in the free troposphere (currently layers 2,3..)
% contabs = true or false for including the water vapor continuum absorption
% linewon = whether to keep linewidth adjustment on or off (for real
%          physics = true, for fake physics = false)
% Tsi =  initial surface temperature
% lapsekm = lapse rate in troposphere, K/km
% lapseikm = initial lapse rate in troposphere, K/km, to setup initial temp
%            profile
% ptropo = defined tropopause pressure
% minp = top of atmosphere to consider for radiative calcs, in pressure (Pa)
% ocd = ocean depth in m - for running dynamic simulations
% src = average solar absorbed radiation (over surface area of earth)
% tstep = timestep in seconds 
% nt = number of timesteps
% ploton = whether the plot is run or not - lots of other plots are
%         generated via separate programs

% ====== Output variables (returned from function) ====================
% vt(numv) = wavenumber vector
% tau(numz-1,numv) = optical thickness by layer and by wavenumber
% fluxu = upward flux at TOA
% fluxd = downward flux at surface
% ztropo = height of tropopause
% z(numz-1) = height of each layer
% dz(numz-1) = thickness of each layer
% p(numz-1) = pressure of each layer
% rho(numz-1) = density of each layer
% mixh2o(numz-1) = water vapor mixing ratio of each layer
% zb(numz) = height at each boundary
% pb(numz) = pressure at each boundary
% Tb(numz) = temperature at each boundary
% rhob(numz) = density at each boundary
% Tinit(numz-1) = starting temperature of each layer
% T(numz-1,nt) = temperature of each atmosphere layer at each time step, T(1,:)=Tinit
% Ts(nt) = temperature of ocean
% dE(numz-1,nt) = change in energy each time step in each layer
% dEs(nt) = change in energy each time step in ocean
% dCE(numz-1,nt) = change in convective heat each time step upward to each
%               layer (1=from ocean to atmosphere layer 1)
% radu(numz,numv) = upward flux at each boundary, boundary 1 = surface
% radd(numz-1,numv) = downward flux at each boundary 
% emitu(numz-1,numv) = emitted radiation from within each layer, layer 1= first
%                      atmospheric layer
% sheat(numz-1) = absorbed solar in each layer in W/m^2
% surfe(nt) = net flux at surface each timestep (+ve downward)
% TOAe(nt) = net flux at TOA each timestep (+ve downward)
% TOAf(numz,numv) = TOA flux contributed from each boundary
% TOAtr(numv) = surface radiation transmitted to TOA
% alr(numz-1,nt) = actual lapse rate between each layer at each time step, in K/km

disp(' ');
disp(['--- New Run v0.10.1 --- ' datestr(now) ' ----']);
disp('  ');

% =========== Basic definitions =====================

% Units in SI unless otherwise noted including all pressure values in Pa
% except for SI, frequency in cm^-1
p0=1.013e5; % std pressure for the HITRANS database in Pa
T0=296; % std temperature for HITRANS database in K
Na=6.02e23; % Avogradro's number
mair=28.96e-3; % molar mass of air
% mh2o=18.02e-3; % molar mass of water vapor
diff=1.66; % diffusivity approximation
ems=1.0; % emissivity of surface
cp=1005; % cp (specific heat cap at constant pressure) of air
cpw=4180; % cp of air, J/kg.K
rhow=1000; % density of water, kg/m^3
solaratm=true; % solar heating of the atmosphere, currently very parameterized
convadj=true; % if true, convective adjustment to lapse rate = lapse
convloop=3; % no of times to repeat convective loop to get lapse rate correct
iso_strato=false; % if true, fixed and isothermal stratospheric temperature
               % if solaratm is true, this should be set to false
lapse=lapsekm/1000; % lapse rate in K/m
lapsei=lapseikm/1000; % initial lapse rate in K/m 
lapsez=ones(1,numz-1)*lapse; % lapse rate for convective adjustment can be
                 % different for each layer, current all set to 'lapse'
print_layers=false; % if true, prints out z, p, T, rho for each layer
windmax=10000/8; windmin=10000/12; % 'atmospheric window' region in wavenumber
                         % for "curiosity value calculation
% set up a few print strings
if contabs
    conttext='Continuum included';
else
    conttext='No Continuum';
end
if convadj
    convtext='With convective adjustment';
else
    convtext='No convective adjustment';
end
if linewon
    linetext=' Linewidth depends on p,T;  ';
else
    linetext=' Constant linewidth;  ';
end
dbh=false;  % debug heat stuff added in 0.9.8, if true print a lot out
dbh1=true; % next level of debugging

% =========== Define wavenumber ranges ==============

vmin=200; % min wavenumber to consider (overall)
vmax=2500; % max wavenumber to consider (overall)
% because absorption lines below the lower boundary (and above the upper
% boundary) can still affect the wavenumbers under consideration we need to
% extend the boundaries of which absorption lines to consider
% rvmin=1; % ratio below lower boundary to consider - not useful for a wide range
% rvmax=1; % ratio above upper boundary to consider

vt=vmin:dv:vmax;  % vt = wavenumbers we will calculate optical depth for
numv=length(vt);  % number of wavenumbers

% =========== Read in GHG data ======================

fprintf('%s', 'Loading HITRAN data.. '); 

% names for the HITRAN molecules up to molecule 6, need to be 3 characters
% each because of how Matlab handles strings
Hmols=['H2O'; 'CO2'; 'O3 '; 'N2O'; 'CO '; 'CH4';]; 

% atmospheric proportions of HITRAN isotopes up to molecule 6, data from
% Rothman et al (2005) table 6, vector 'ison' extracts the values needed
Hisoprop=[0.9973 0.0020 0.0004; 0.9842 0.0111 0.0039; 0.9929 0.0040 0.0020; ...
    0.9903 0.0036 0.0036; 0.9865 0.0111 0.0020; 0.9883 0.0111 0.0006]; 

% select data on GHGs from vector "mol", isotopes to consider, define isotope ratios

% how many molecules are being considered
nmol=length(mol);
% select the molecule names being used from the list in 'mol'
mols=Hmols(mol,:);
% select isotopologues for each molecule, each molecule, m, will only be
% considered to the depth of ison(m) defined in the function parameters
isoprop=Hisoprop(mol,1:max(ison));
            
% Now read in the line data via 'Hitran_read' function

% v=line position, S=line strength, iso=isotopologue, gama = air-broadened
% half-width, nair=temperature-dependence exponent for gama

% We don't know the final size of the vectors and some GHGs have very large
% lists, while others are very small so space considerations mean creating
% a [1 x total lines] array rather than [nmol x max of largest]
for i=1:nmol
    if i==1  % first value established the vector
        
        [ v S iso gama nair ] = Hitran_read_0_2(mol(i), vmin, vmax, ison(i));
        % now set an identifier
        molx=ones(1,length(v))*mol(i); % identifies all these values as this molecule
        
    else    % now subsequent values get appended
        [ v1 S1 iso1 gama1 nair1 ] = Hitran_read_0_2(mol(i), vmin, vmax, ison(i));
        
        molx1=ones(1,length(v1))*mol(i); % identifies all these values as this molecule
        v=[v v1]; iso=[iso iso1]; gama=[gama gama1]; S=[S S1]; nair=[nair nair1];
        molx=[molx molx1];
    end
end

fprintf('%s', 'finished.. '); 
% =========== Finished reading GHG data ======================

% =========== Define standard atmosphere against height =============

% ---- First create a "high resolution" atmosphere
% zr = height, pr = pressure, Tr = temperature, rhor = density

ps=1.013e5; % define surface pressure

maxzr=50e3; % height of high resolution atmosphere
numzr=5001; % number of points used to define high res. atmosphere
zr=linspace(0,maxzr,numzr); % height vector from sea level to maxzr

% use 'define_atmos' function to determine pr, Tr, rhor & ztropo (height of
% tropopause)
[pr Tr rhor ztropo] = define_atmos_0_5(zr,Tsi,ps,ptropo,lapsei);  
% for consideration - if the radiative-convective model changes temperature
% significantly, should the pressure be re-adjusted?

% ---- Second, create "coarser resolution" atmosphere - this reduces 
% computation requirements for absorption & emission of radiation
% - this atmosphere has numz boundaries and numz-1 layers

% z, p, Tinit, rho; subset of values used for RTE calcs

% We divide the atmosphere into approximately equal pressure changes
% except for first layer which is the boundary layer at pressure = blp 
% with different humidity (BLH)

% this part of the code was fixed on Jan 9, 2013 for v0.9.2, previously 
% (and up to article 4 in the "Visualization" series) created an arbitrary
% thickness layer above boundary layer due to poor code
dp=(blp-minp)/(numz-2); % finds the pressure change for each height change

zi=zeros(1,numz); % zi = lookup vector to "select" heights, pressures etc
zi(1)=1; % make first value the surface value
zi(2)=find(pr<=blp, 1); % gets the location of boundary layer top edge
for i=3:numz % locate each value
    zi(i)=find(pr<=(pr(zi(2))-(i-2)*dp), 1); % gets the location in the vector where 
                                % pressure is that value
end

% now create the vectors of coarser resolution atmosphere
% zb is height of boundaries, zb(1) = surface; zb(numz) = TOA
% T, p, rho are all the midpoint (pressure) between the boundaries

zb=zr(zi);   % height at boundaries
pb=pr(zi);   % pressure at boundaries
Tb=Tr(zi);   % starting temperature at boundaries
rhob=rhor(zi);  % density at boundaries

% now calculate density, pressure, temperature and water vapor saturation
% mixing ratio at midpoint of each layer - midpoint by pressure
dz=zeros(1,numz-1);z=zeros(1,numz-1);Tinit=zeros(1,numz-1);
p=zeros(1,numz-1);rho=zeros(1,numz-1);mixh2o=zeros(1,numz-1);
im=zeros(1,numz-1); % index for getting midpoints at midpoint pressure
sheat=zeros(1,numz-1); % W/m^2 solar heating of each layer of the atmosphere
sheath2o=zeros(1,numz-1); % W/m^2 solar heating by water vapor of each layer of the atmosphere

% calculate pressure in midpoint of layer
for i=1:numz-1 
    p(i)=(pb(i+1)+pb(i))/2; % pressure in midpoint of layer
    dz(i)=zb(i+1)-zb(i); %  thickness of each layer
end

% lookup midpoint values for z, T, rho at the midpoint pressure
for i=1:numz-1 
    im(i)=find(pr<=p(i), 1); % gets the location in the vector of midpoint pressure
end

z=zr(im); % calculate height of midpoint pressure
Tinit=Tr(im); % temperature of midpoint pressure
rho=rhor(im); % density of midpoint pressure
iztropo=find(pb<ptropo,1)-1; % location in the p vector of the first layer above the tropopause

% calculate Heat capacity for each layer, Cp = rho x dz x cp in J/K
Cp=zeros(1,numz-1);
Cp=rho.*dz.*cp; % of each atmospheric layer
Cps=rhow*ocd*cpw; % of ocean

for i=1:numz-1 
    % now calc mixing ratio in molecules for water vapor at prescribed RH
    % = RH * es / p
    % currently satvaph2o() gives es=610.94.*exp(17.625.*Tc./(Tc+243.04)); where Tc in 'C
    if i==1
        mixh2o(i)=BLH*satvaph2o(Tinit(i))/p(i); 
    else
        mixh2o(i)=FTH*satvaph2o(Tinit(i))/p(i);
    end
end
   
if solaratm  % if we are using solar heating of the atmosphere
    % ozone and water vapor, first pass, using solar heating rates from 
    % Petty (2006), p.313
    % first ozone, use 0'C/day at 10km, straight line through 2'C/day at 
    % 30km and convert to W/m^2
    sheat=(z>=10000).*((z./1000-10)/10).*Cp/86400;
    % now water vapor - this will be the most badly modeled due to the
    % variability of water vapor - convert to W/m^2
    sheath2o=(((z<5000).*(z./1000*.6/5+.7))+(z>=5000 & z<9000).*((9000-z)./1000*1.1/4+.3)...
    +(z>=9000 & z<15000).*((15000-z)./1000*.3/5)).*Cp/86400;
    sheat=sheat+sheath2o;    
end

if print_layers        % display values at each pressure
    disp(' ');
    disp(['dp= ' num2str(dp)]);
    for i=1:numz-1
        disp(['p= ' num2str(p(i)/100,'%4.0f') ', z= ' num2str(z(i),'%4.0f')...
            ', T= ' num2str(Tinit(i)) ', rho= ' num2str(rho(i),'%4.2f')]);
    end
    for i=1:numz
        disp(['pb= ' num2str(pb(i)/100,'%4.0f') ', z= ' num2str(zb(i),'%4.0f')]);
    end
    disp(['Pressure of tropopause layer = ' num2str(z(iztropo)) ', at ' num2str(iztropo)]);
end

% =========== Finished defining standard atmosphere against height ======


% =========== Absorption and Emission - each layer of the atmosphere, i =====
% note: work in cm for volumes and distances (absorption coefficients are in cm)

% now set optical thickness, [layers x numv]
fprintf('%s', 'Calc optical thickness each layer.. '); 
tau=zeros(numz-1,numv); % optical thickness 
              
% ----------- Each layer ------------------------
for i=1:numz-1 
    fprintf('%d %s', i, ' '); % display layer being calculated (this section takes the longest)
   
    na=(Na*rho(i)/mair)/1e6; % number of air molecules per cm^3
    d=100*dz(i); % path length in cm 
    
    % and so for this slab of depth, d:
    % ----------- Iterate through each GHG for this slab, m --------------
    for m=1:nmol
        % fprintf('%d %s', m, ' '); % display molecule being calculated
        if mol(m)==1  % if water vapor, special case
            mix(m)=mixh2o(i); % precalculated for each layer using prescribed RH
            % disp(['w.v. mixing ratio at ' num2str(p(i)/1e2) ' mbar is ' num2str(mix(m)*1e3)]);
            if contabs % if using continuum absorption
                % method from Pierrehumbert 2010, p.260, uses svp & units
                % in m2/kg
                %disp(['Continuum for layer ' num2str(i)]);
                es=satvaph2o(Tinit(i)); % get sat.vap. pressure in Pa
                %disp(['Sat vap pressure = ' num2str(es)]);
                sig=continuum1000(vt,Tinit(i)); % get capture cross section in m2/kg 
                % ** note non-std units ** and values are only valid for 
                % range defined in function continuum1000                
                if i==1
                    RH=BLH; % use the correct relative humidity
                else
                    RH=FTH; % use the correct relative humidity
                end
                % This value of optical thickness will be most sensitive
                % to temperature changes when time steps take place
                % - so later need to consider having this recalculated after 
                % set dT'C change in temperature in a layer
                tau(i,:)=tau(i,:)+sig.*pi/100*(es*RH)^2/(1e4*461.4.*Tinit(i)); 
            end
        end
        im=find(molx==mol(m)); % the index for all values of this GHG
        immax=length(im); % the number of lines for this GHG
        %disp(['Layer ' num2str(i) '. Mixing ratio for molecule ' num2str(m) ' = ' num2str(mix(m))]);
        % ------- Iterate through each absorption line for this GHG, j ----
        
        for j=1:immax  % each absorption line
            % im(j) is the index for v, S, etc
            % v(im(j))=line center, S(im(j))=line strength, gama(im(j))=half width
            % now a code inefficient method - calculate the profile for each
            % across the entire wavenumber range
            
            % for this one line we need to find iso # and therefore the relevant
            % proportion then x mixing ratio x no of air molecules
            nummol=isoprop(m,iso(im(j)))*mix(m)*na;
            % then calc the actual line width for this temp & pressure
            if linewon % normal physics
                ga=gama((im(j))).*(p(i)/p0).*(T0/Tinit(i)).^nair((im(j)));
            else  % non-real physics for comparison
                ga=gama(im(j));
            end
            
            % note that if we adjust temperature considerably over timesteps 
            % then may need an iteration of complete routine because line 
            % widths change with temperature
            
            % Pekka's code improvement for v0.9.5
            dt1=1./((vt-v(im(j))).^2+ga^2); % line shape across all wavenumbers
            tau(i,:)=tau(i,:)+nummol*S(im(j))*ga*dt1; % change to tau for
            % this layer and line for all wavenumbers
        end % end of each absorption line, j
    end % end of each GHG, m
    
    tau(i,:)=d/pi*tau(i,:); % now include the 3 constants
    tau(i,:)=diff*tau(i,:);
end % end of each layer, i

disp(' '); % to produce a newline

% =========== Calculate absorption, emission & temperature changes =========

Ts=zeros(1,nt); % define array to store ocean temperature 
T=zeros(numz-1,nt); % define array to store T for each atmospheric level and time step
dEs=zeros(1,nt); % energy change for ocean for each time step
dE=zeros(numz-1,nt); % energy change for each atmospheric level
dCE=zeros(numz-1,nt); % convective energy tracking

sr=ones(1,nt)*src; % solar flux at TOA vs time (later can vary with time)
sr0=sr-sum(sheat); % define solar flux absorbed at surface (=solar at  
                   % TOA - atmospheric absorbed)
                  
T(:,1)=Tinit;   % load temperature profile for start of scenario
Ts(1)=Tsi;   % ocean temperature for first time step (this could have been the bottom 
             % layer of the atmospheric model, but feature added after code developed 
      
TOAe=zeros(1,nt); % TOA instantaneous flux balance vs time
surfe=zeros(1,nt); % Surface instantaneous flux balance vs time
             
% i = layer, k = wavenumber
tran=zeros(numz-1,numv); abso=zeros(numz-1,numv); % set array
for i=1:numz-1   % each layer
    for k=1:numv   % each wavenumber interval
        tran(i,k)=exp(-tau(i,k));  % transmissivity = 0 - 1
        abso(i,k)=(1-tran(i,k));  % absorptivity = emissivity = 1-transmissivity
    end
end
    
    
% =========== Main loops to calculate TOA spectrum & flux =====

% first, we timestep
% second, we work through each layer
% third, through each wavenumber
% fourth, through each absorbing molecule
% currently calculating surface radiation absorption up to TOA AND
% downward radiation from TOA (at TOA = 0)

% h = timestep, i = layer, j = wavenumber
for h=2:nt  % main iterations to achieve equilibrium
    if dbh
        disp(['Timestep ' num2str(h)]);
        %fprintf('%d %s', h, ' '); % display current timestep being calculated
    end
    
    radu=zeros(numz,numv); % initialize upward intensity at each *boundary* and wavenumber
    radu1=zeros(numz,numv); % initialize curiosity version of radu (no emission)
    emitu=zeros(numz,numv); % initialize emission upward for each *layer* and wavenumber
    
    radd=zeros(numz,numv); % initialize downward intensity at each *boundary* and wavenumber
    emitd=zeros(numz,numv); % initialize emission downward for each *layer* and wavenumber
    radu(1,:)=ems.*planckmv(vt,Ts(h-1));  % upward *surface* radiation vs wavenumber
    radu1(1,:)=radu(1,:); % evaluating radiation transfer with no emission - for interest
    radd(end,:)=zeros(1,numv);  % downward radiation at TOA vs wavenumber (=zero)
    % units of radu, radd, emitu, emitd are W/m^2.cm^-1, i.e., spectral emissive power
    
    % Upwards spectral emissive power
    for i=1:numz-1   % each layer
        for j=1:numv   % each wavenumber interval
            
            % calc intensity (each wavenumber) at next boundary
            % = incoming * transmissivity + emission
            % emission upward = Planck formula x emissivity (=absorptivity)
            emitu(i,j)=abso(i,j)*3.7418e-8.*vt(j)^3/(exp(vt(j)*1.4388/T(i,h-1))-1);
            % calculate spectral emissive power at next upward boundary
            radu(i+1,j)=radu(i,j)*tran(i,j)+emitu(i,j);
            radu1(i+1,j)=radu1(i,j)*tran(i,j); % transmitted only, for curiosity
            
            % Change in radiated energy = dI(v) * dv (per second)
            % accumulate through each wavenumber
            % if the upwards radiation entering the layer is more than
            % the upwards radiation leaving the layer, then a heating
            dE(i,h)=dE(i,h)+(radu(i,j)-radu(i+1,j))*dv*tstep;
            % pre 0.10; Eabs(i)=Eabs(i)+(radu(i,j)-radu(i+1,j))*dv;
        end  % each wavenumber interval
    end  % each layer
    
    % Downwards spectral emissive power
    for i=numz-1:-1:1   % each layer from the top down
        for j=1:numv   % each wavenumber interval
            % calculate emission downward (same as upward but in case we
            % play around later)
            emitd(i,j)=abso(i,j)*3.7418e-8.*vt(j)^3/(exp(vt(j)*1.4388/T(i,h-1))-1);
            % calculate spectral emissive power at next upward boundary
            radd(i,j)=radd(i+1,j)*tran(i,j)+emitd(i,j);
            dE(i,h)=dE(i,h)+(radd(i+1,j)-radd(i,j))*dv*tstep;            
        end  % each wavenumber interval
        dE(i,h)=dE(i,h)+sheat(i)*tstep; % add in solar absorbed for this layer
        
        dT=dE(i,h)/Cp(i); % change in temperature = dQ/heat capacity
        if dbh
            disp(['Layer ' num2str(i) ', dE = ' num2str(dE(i,h)) ', dT= ' num2str(dT)]);
        end
        
        if iso_strato && i>iztropo  % if we want to keep stratosphere at fixed temperature
            % but allow whole stratosphere temp to move in this version,
            % defined by the value of temperature in the tropopause layer
            T(i,h)=T(iztropo,h-1);  % layers above fixed to last iteration of tropopause layer
            % calculating from top down so can't use current time period value
            
            % **** need to account for movement of heat in this part of the
            % atmosphere under this scenario - not yet done
        else
            T(i,h)=T(i,h-1)+dT; % calculate new temperature
            
            if T(i,h)>500  % picks up finite element problem
                disp(['Terminated at h= ' num2str(h) ', z(i)= ' num2str(z(i)) ', i = ' num2str(i)]);
                disp(['time = ' num2str(h*tstep/3600) ' hrs; = ' num2str(h*tstep/3600/24) ' days']);
                disp(datestr(now));
                return
            end
        end
        % might need a step to see how close to an equilibrium we are
        % getting - not yet implemented because this part of routine is so fast
    end  % each layer
    
    % now ocean heat changes (via radiation) = time x (Solar + Rdown -Rup)
    dEs(h)=(sr0(h)+(sum(radd(1,:))-sum(radu(1,:)))*dv)*tstep;
    % Temperature change = Energy change / Cp
    Ts(h)=Ts(h-1)+ dEs(h)/Cps;
    if dbh
        disp(['Ocean dE = ' num2str(dEs(h)) ', new Ts= ' num2str(Ts(h))]);
    end
    
    % now apply convective adjustment
    if convadj==true  % if convective adjustment chosen..
        
        for j=1:convloop % we need to iterate to a solution
            tc=zeros(1,numz-1); % temporary value of convective energy
            
            % Have already worked out the new temperatures for timestep,h,
            % based on radiated energy from previous time step, so use this
            % timestep and adjust for convection
            % Problem is 3 simultaneous equations with 3 unknowns because both
            % the temperature above and below change and the lapse rate must be
            % valid for the new temperatures
            
            % First from surface to layer 1, slightly different code
            if (Ts(h)-T(1,h))/z(1)>lapsez(1) % if lapse rate is too high
                
                tc(1)=(Ts(h)-T(1,h)-z(1)*lapsez(1))/(1/Cps+1/Cp(1));
                if tc(1)<0    % should always be positive ***
                    disp(['Error in convective adj. layer 1, h= ' num2str(h)...
                        ', i= ' num2str(i) ', dCE= ' num2str(tc(1))]);
                end
                
                if dbh
                    disp(['Lapse to layer 1= ' num2str((Ts(h)-T(1,h))/z(1)*1000) 'K/km, newT= '...
                        num2str(newT) ', old atm T= ' num2str(T(1,h)) ', T(ocean)= ' num2str(Ts(h))]);
                end
                
                dEs(h)=dEs(h)-tc(1); % reduce heat tracking stored in ocean
                dE(1,h)=dE(1,h)+tc(1); % increase heat tracking stored in atmos layer 1
                T(1,h)=T(1,h)+tc(1)/Cp(1); % calc revised atmospheric temperature
                Ts(h)=Ts(h)-tc(1)/Cps;  % calc revised ocean temperature
                
            end
            % Now for all the atmospheric layers
            for i=2:numz-1
                if (T(i-1,h)-T(i,h))/(z(i)-z(i-1))>lapsez(i)  % too cold, convection will readjust
                    % calculate the convective heat transfer that satisfies the
                    % simulataneous equation
                    tc(i)=(T(i-1,h)-T(i,h)-(z(i)-z(i-1))*lapsez(i))/(1/Cp(i)+1/Cp(i-1));
                    
                    if tc(i)<0    % should always be positive ***
                        disp(['Error in atm convective adj, h= ' num2str(h)...
                            ', i= ' num2str(i) ', dCE= ' num2str(tc(i))]);
                    end
                    if dbh
                        disp(['Lapse from layer ' num2str(i) ' to ' num2str(i-1)...
                            ' = ' num2str((T(i-1,h)-T(i,h))/(z(i)-z(i-1))*1000) ' K/km, newT= ' ...
                            num2str(newT) ', old atm T= ' num2str(T(i,h))]);
                    end
                    
                    dE(i-1,h)=dE(i-1,h)-tc(i); % reduce heat tracking stored in layer below
                    dE(i,h)=dE(i,h)+tc(i); % increase heat tracking stored in this layer
                    T(i,h)=T(i,h)+tc(i)/Cp(i); % set revised atmospheric temperature
                    % also adjust atmospheric layer below (has lost heat)
                    T(i-1,h)=T(i-1,h)-tc(i)/Cp(i-1);
                    
                end
            end
            % now accumulate the convective adjustments
            dCE(:,h)=dCE(:,h)+tc';
        end
    end
    
    if h==2 || h==nt/2 % if on first time step or middle
        % print out initial results of flux
        disp([' Time= ' num2str(h*tstep/86400,'%4.2f') ' days, Flux up at TOA = '...
            num2str(sum(radu(end,:))*dv,'%4.1f') ' W/m^2, Flux down at surface = ' ...
            num2str(sum(radd(1,:))*dv,'%4.1f') ' W/m^2']);
    end
    
    % instantaneous imbalance at TOA (+ve downward) in W/m^2 = (solar rate - olr rate)
    TOAe(h)=sr(h)-sum(radu(numz,:))*dv; 
    % instantaneous imbalance at surface in W/m^2 +ve downward = solar + DLR - Surface
    % emitted - convected (per second)
    surfe(h)=sr0(h)+sum((radd(1,:))-radu(1,:))*dv-dCE(1,h)/tstep; 
    
    % 1st law of thermodynamics check; heat gained = Es +sum(E)
    dqgain=dEs(h)+sum(dE(:,h)); % net energy absorbed in the time step
    if abs(TOAe(h)*tstep-dqgain)>1 % if more than 1W/m^2 discrepancy
        disp(['Time step ' num2str(h) ', Net Energy missing = ' num2str(TOAe(h)*tstep-dqgain)]);
    end
end   % ---- timestep iterations

% =========== Finish loops to calculate TOA spectrum & flux =====
disp(' '); % to produce a newline

fluxu=sum(radu(end,:))*dv;   % calculate the final TOA flux
fluxd=sum(radd(1,:))*dv;   % calculate the final DLR total

% =========== Calculate some curiosity values ===============

% flux transmitted from surface and in "atmospheric window"
% calculate the surface radiation transmitted to TOA (integral with dv)
TOAtr=dv*radu(1,:)*exp(-sum(tau))'; 
iw=find(vt>=windmin & vt<=windmax); % find the window region in the vector

% flux proportions transmitted from each layer & from the surface, by
% wavenumber
stau=zeros(numz-1,numv); % optical thickness by wavenumber summed from top down
TOAf=zeros(numz,numv); % TOA flux proportion, has to include surface so is number of layers + 1
TOAf(numz,:)=dv*emitu(numz-1,:); % get the top layer, no attenuation
stau(numz-1,:)=tau(numz-1,:); % set the first tau value for the top layer

for i=numz-2:-1:1
    % flux from layer i+1 transmitted to TOA is emitu(i)*stau(i+1)
    % needed to shift everything up 1 layer so that the surface can be
    % included
    TOAf(i+1,:)=dv*emitu(i,:).*exp(-stau(i+1,:));    
    % sum tau going downwards
    stau(i,:)=stau(i+1,:)+tau(i,:); %
end
TOAf(1,:)=dv*radu(1,:).*exp(-stau(1,:)); % radu(1,:)= surface intensity (below the bottom layer of atmosphere)
    
% Calculate the lapse rates for each layer at each timestep
alr=zeros(numz-1,nt);
alr(1,:)=1000*(Ts-T(1,:))./z(1); % ocean to layer 1
for i=2:numz-1
    alr(i,:)=1000*(T(i-1,:)-T(i,:))./(z(i)-z(i-1)); % value in K/km
end
% Print out inputs to simulation
disp(['Tsi= ' num2str(Tsi) ', Lapse rate= ' num2str(lapsekm) ', ' conttext ', BLH= ' num2str(BLH*100)...
    '%, FTH= ' num2str(FTH*100) '%, blp = ' num2str(blp/100) 'hPa, TOA = ' num2str(minp/100) 'hPa']);
disp([num2str(numz-1) ' layers, dv= ' num2str(dv) 'cm-1,  ' linetext num2str(nt) ...
    ' timesteps of ' num2str(tstep/3600/24,'%4.2f') ' days']);
disp(['Solar absorbed= ' num2str(src) ' W/m^2, Absorbed in atmosphere= ' ...
    num2str(sum(sheat),'%4.2f') ' W/m^2']);
disp(convtext);

% Print out GHG concentrations
for i=1:nmol
    if mol(i)>1 % i.e. is not water vapor, which is printed via BLH, FTH
        fprintf([mols(i,:) '= ' num2str(mix(i)*1e6) ' ppm,  '],'%s');
    end
end
disp(' '); 

% Print out various flux values
disp(' ');
disp([' Final Time= ' num2str(h*tstep/86400,'%4.2f') ' days']);
disp(['Flux up at TOA = ' num2str(fluxu,'%4.1f') ' W/m^2, Flux down at surface = ' ...
    num2str(fluxd,'%4.1f') ' W/m^2']);
disp(['TOA transmitted flux= ' num2str(TOAtr,'%4.1f') ' W/m^2, Surface emission= ' ...
    num2str(sum(radu(1,:)),'%4.1f') ' W/m^2, Window transmission= ' ...
    num2str(sum(radu1(numz,iw))/sum(radu(1,iw))*100,'%4.1f') ' %']);
disp(['Starting flux imbalance TOA= ' num2str(TOAe(2),'%4.2f') ' W/m^2,  Final imbalance TOA= ' ...
    num2str(TOAe(end),'%4.2f') ' W/m^2']);

% Print out temperature values & lapse rate
disp(' ');
disp('Temperature change, start to finish ');
for i=numz-1:-1:1
    disp(['Layer ' num2str(i) ' = ' num2str(T(i,nt)-T(i,1),'%4.2f')]);
end
disp(['Temp change ocean  = ' num2str(Ts(nt)-Ts(1),'%4.2f')]);
disp('Final lapse rate ');
for i=numz-1:-1:2
    disp(['Lapse rate ' num2str(i-1) '-' num2str(i) ' = ' ...
        num2str(alr(i,end),'%4.2f') ' K/km']);
end
disp(['Lapse rate ocean - 1 = ' num2str(alr(1,end),'%4.2f') 'K/km']);
    
  
% =========== Plots, if needed ==================
if ploton
    figure(2)
    zz=[0 z]; % add the surface to the height vector to make it possible to plot
    plot(sum(TOAf'),zz/1000,'r*')
    xlabel('W/m^2 contribution to TOA flux')
    ylabel('Height of layer, km')
    grid on
    
    figure(1)
    % graphs of temperature and energy
    
    tv=2:nt; % time vector
    iz=[1 2 4 7 10 12]; % atmospheric layers to consider (to reduce clutter)
    % first graph - temperatures of a few layers    
    nump=length(iz); % number of items plotted
    textleg(1)={'Ocean'}; 
    for i=1:nump 
        textleg(i+1)={[num2str(iz(i))]};               
    end
    
    subplot(2,2,1),plot((1:nt)*tstep/86400, Ts-Ts(1), ...
        (1:nt)*tstep/86400, T(iz,:)-(repmat(T(iz,1),1,nt)))
    ylabel('Temperature Anomaly, K')
    xlabel('Time')
    grid on
    title(['Temperature anomaly, initial Ts=' num2str(Tsi),'K, Lapse=' num2str(lapsekm)])
    %legend('Ocean','1','2','3','4','5','6','7','8','9', '10')
    legend(textleg);
    
    % second graph - TOA & surface imbalance
    subplot(2,2,2),plot(tv*tstep/86400,TOAe(tv),tv*tstep/86400,surfe(tv))
    xlabel('Time, days')
    ylabel('Flux imbalance, W/m^2')
    ylim([-5 5])
    legend('TOA','Surface')
    grid on
    
    % third graph - rate of energy change each layer
    subplot(2,2,3),plot(tv*tstep/86400,dEs(tv)/tstep,tv*tstep/86400,dE(iz,tv)/tstep)
    xlabel('Time, days')
    ylabel('Instantaneous Energy Gain, W/m^2')
    ylim([-5 5])
    grid on
    title(['Each time step= ' num2str(tstep/86400,'%3.2f') ' days'])
    legend(textleg);
    
    % fourth graph - convective flux between layers
    subplot(2,2,4),plot(tv*tstep/86400,dCE(:,tv)/tstep)
    xlabel('Time, days')    
    ylabel('W/m^2')
    grid on
    title(['Convective flux between Layers, Each time step= ' num2str(tstep/86400,'%3.2f') ' days'])
    legend('Ocean->Layer 1', '1-2','2-3','3-4','4-5', '6-7','7-8','8-9','9-10');
    
    figure(3)
    % actual lapse rate to check
    subplot(1,2,1),plot((1:nt)*tstep/86400,alr)
    xlabel('Time, days')
    ylabel('Lapse rate, K/km')
    ylim([6 7])
    grid on
    legend('Ocean->Layer 1', '2-3','3-4','4-5', '6-7','7-8','8-9','9-10')
    % vertical temperature profile at 3 times
    subplot(1,2,2),plot(T(:,1),z/1000,T(:,ceil(nt/2)),z/1000,T(:,end),z/1000)
    legend('Start','Mid','Finish')
    ylabel('Height, km')
    xlabel('Temperature')
end
% ==================================================

disp(['---- End of Run ---- ' datestr(now) ' ----']);